## Slide 1: Process controll –Hyperdrive Project
Joachim Raffaele Bono Elise Høimyr Séverine Oppliger
Group D

## Slide 2: Demo
TODO: insert a video in case it doesn’t work

## Slide 3: GUI
Python (uses Tkinter)
Java (uses Swing)

## Slide 4
Java Implementation (1/2) - Classes
Main
SetupVehicleManager
SteeringController
SteeringModel
View
VehicleInfoController
VehicleInfoModel
MqttHandler
MessageHandler
MessageListener
Utilities
MVC architecture
Connect to vehicle through MQTT broker
Steering thread
VehicleInfo thread
Manage communication between the application and the MQTT broker
Recipient of the last message published in a given topic to which we are subscribed
Manage MessageListeners and handle incoming messages (store them in the appropriate MessageListener instance)
Control speed, lane offset, lights + (de)toggle emergency stop
Retrieve info about connection status, measured speed, trackId, battery level + estimate if turning
Broker discovering ?
If no, «discover»: true
Vehicle among recognized vehicles ?
Connect vehicle
Is vehicle ready ?

## Slide 5: Java Implementation (2/2) – MVC
Model
View
Controller
Steer
Retrieve vehicle info
Connection status
Measured speed
Turning status
Current track id
Battery level
Thread
On
Off
Emergency
Wished speed
Wished lane offset
Front lights / Back lights
Emergency status
MQTT
MQTT
Observable
Observer
Observable
Observer

## Slide 6: Difficulties
GUI:
  Sliders: action (publish) at each step while we move it (not only when mouse realised)
   fixed on Java but seems impossible on Python
Battery status: is not really reliable (shows 80 when battery is fast empty)
Concurrent programming: no Java interaction with MQTT emergency topic
 no external emergency activation detected